## Slide 1: EE-2003 Computer Organization and Assembly Language Fall2025
Department of Computer Science/Software Engineering/Artificial Intelligence

## Slide 2: Course Information
Text and Reference Books
  Course Outline available on SLATE/Google Class Room
Course Objectives and outcomes
  Available on SLATE/Google Class Room
Course Contents

## Slide 3: Course Information
Lecture material will be available on SLATE
Regularly review the lectures discussed in the class
Prior knowledge of Courses required
  ITC and DLD

## Slide 7: Languages Generations!

## Slide 8
Some Basics- Quick Review

## Slide 9: Lecture Overview
Numbering & Coding Systems
Digital Primer
Semiconductor Memory

## Slide 10: Numbering & Coding Systems
Decimal, Binary and Hexadecimal Number Systems
Interconversion Between these Systems
-converting from decimal to binary and binary to decimal
-converting between binary and hex
-converting from hex to decimal
-addition/subtraction of binary and hex numbers

## Slide 17: Digital Primer
What is digital logic?
Logic gates are put together to form simple digital circuits, i.e Adders, subtractor, decoder etc

## Slide 18: SemiConductor Memory

## Slide 19: Important Terminologies !

## Slide 20: RAM & ROM

## Slide 21: Organization of Computers
Data Bus
RAM/ROM
I/O Device
Address Bus
Control Bus
CPU

## Slide 22: Organization of Computers
Address Bus
  Size of Memory accessible by Processor
  64 K locations = 16 bit address
Data Bus
  Chunk of Data accessible
  8-bit data Bus accesses 1 byte
  16-bit data Bus accesses 2 bytes
RAM
  Stores program and data which is not permanent
ROM
  Stores permanent code and data

## Slide 23: Internal Organization of Computers
CPU – Process information stored in memory
I/O – Provides mean of communicating with CPU
Memory- RAM & ROM
-RAM is a volatile and is used by the computer for temporary storage of a program that is running.
-ROM is a non-volatile, information is permanent and can not be changed by the user.
CPU is connected to I/O’s & Memory through buses.

## Slide 24: Address, Data & Control Bus
Address Bus – For a device to be recognized by the CPU it must be assigned an address.
Address assigned to a given device must be unique.
CPU puts the address on the address bus, and the decoding circuity finds the device.
Data Bus- CPU uses data bus either to get data from or to send the device.
Control Bus –CPU use the control bus to provide the read or write signal to the device to indicate if the CPU is asking for information or sending information.

## Slide 25: More about Data Bus..
More data buses available the better and expensive the CPU will be..
Data buses are bidirectional.
Processing power of CPU is related to the size of its buses.

## Slide 26: More about Address Bus
More address buses present, the larger device can be addressed. Number of address buses determines the number of locations with which it can communicate
CPU with 16 address lines can provide of addressable memory.

## Slide 27: CPU and Its relation to RAM & ROM
For a CPU to process information the data must be present in ROM or RAM.
provides fixed and permanent information such as tables for character patterns or initialization programs.
RAM stores temporary information that can be changed with time such as various versions of OS and application packages etc.
CPU gets information to be processed from RAM or ROM, if its not there it request the secondary storage such hard drives and transfer the information to RAM.

## Slide 28: Memory Capacity
Number of bits that semiconductor memory can store is chip capacity.

## Slide 29: Memory Organization
A memory chip contains locations-
Each location contains -
Entire chip will contain

## Slide 30: Examples.. Finding Capacity & Organization of memory..

## Slide 31: Capacity & Org. of Some UV-EPROM Chips…

## Slide 32: Inside CPU
The CPU uses registers to store information temporarily
Registers can be 8-bit, 16-bit, 32-bit or even 64-bit
More and bigger registers, the better the CPU.
CPU cost is increased with more and bigger registers.
CPU is having ALU for performing athematic functions
Program counter in the CPU points to the address of the next instruction to be executed.
Instruction decoder in CPU interpret the instruction fetch into the CPU
CPU capable of understanding more instructions requires more transistors to design

## Slide 33: Example Internal Working of CPU

## Slide 34: Adding three numbers
Add numbers 21, 42 and 12
Which system unit will add the two numbers? (Register, ALU, Control Unit)
The ALU
Before the ALU can add the numbers, where should the numbers be temporarily stored?
Registers
Assume that CPU has four registers A, B, C & D

## Slide 35: Adding three numbers
What is the range of memory address and size of data if the CPU can access data through an 8-bit data bus and 16-bit address bus?
It can access one byte of instruction or data
Address range is 0000 to FFFF H

## Slide 36: Adding three numbers
The CPU performs the following actions to add the three numbers
  Put 21 into A register
  Add to register A the value 42
  Add to register A the value 12
The program instructions which implement the above actions are stored in the memory
The code to move the value to register A is
  1011 0000 (B0 H)
The code to add the value to register A is
  0000 0100 (04 H)

## Slide 37: Adding three numbers
Action Code Data
Move value 21 H into reg. A B0 H 21 H
Add value 42 H to reg. A 04 H 42 H
Add value 12 H to reg. A 04 H 12 H
Where should the program be stored?
In the Memory
At which address should the program be stored?
The first address of the memory
But the start address can be any address
Assume first address where instruction is stored is 1400 H

## Slide 38: Adding three numbers
What is the size of the program? (in bytes)
Seven bytes
Address Instruction
1400 B0
1401 21
1402 04
1403 42
1404 04
1405 12
1406 F4

## Slide 39: Von Neumann vs. Harvard Architecture

## Slide 40: ..
Every microprocessor must have memory space to store program (code) and data.
Code provides instruction to the CPU while data provides the information to be processed.
Buses are used to access the code ROM & data RAM memory spaces.
Early computer used the same buses for both code & data - Von Neumann
Such architecture slow down the processing speed of the CPU….

## Slide 41: ..
Separate buses are used to access code and data- Harvard Architecture